## Slide 1: Inter-calibration RSR Difference Corrections
Benjamin Scarinoa, David R. Doellingb, Arun Gopalana, Thad Cheea, Rajendra Bhatta, and Conor Haneya
aSSAI, One Enterprise Pkwy Ste 200, Hampton, VA 23666 USA
bNASA Langley Research Center, 21 Langley Blvd MS 420, Hampton, VA 23681-2199 USA
CLARREO Pathfinder Inter-Calibration Workshop
16 November 2017 NIA, Hampton, VA

## Slide 2: Outline
Purpose
Spectral Band Adjustment Factor (SBAF)
  Accounts for inter-calibration relative spectral response (RSR), or spectral response function (SRF), disparities
  Overview
  Applications
Online SBAF Tools
  SCIAMACHY
  GOME-2
  Hyperion
  IASI
  AIRS
Other Tools
  Spectral response function comparison tool
  Visible band solar constant comparison tool
  Earth-spectra plotting tool
Summary

## Slide 3: Purpose
Provide SBAF tools for the GSICS and calibration communities
  Goal: Consistent inter-sensor calibration and retrievals
  Customizable
  Based on hyperspectral datasets
  Capture scene conditions during inter-calibration events
  Single web location for SBAFs based on best practices of the community
  Success dependent on feedback
Inputs desired from users
    New/updated/recommended SRFs
    New/recalibrated/updated versions, hyperspectral datasets, and/or paramaters
Welcoming suggestions
    Spectral domains or scene types
    Tool features
      New subsetting options
      Interface changes
    Plotting controls

## Slide 4: NASA Langley Satellite Calibration Webpage
https://satcorps.larc.nasa.gov
https://satcorps.larc.nasa.gov/cgi-bin/site/showdoc?mnemonic=SAT_CALIB_USER

## Slide 5: Spectral Band Adjustment Factor (SBAF)
Derive reference- and target-sensor pseudo radiance/reflectance (Lp) via hyperspectral convolution over each RSR to account for band difference/out-of-band absorption
Derive reference- and target-sensor pseudo radiance/reflectance (Lp) via hyperspectral convolution over each RSR to account for band difference/out-of-band absorption
Every Earth scene has a unique spectral reflectance signature

## Slide 6: Spectral Band Adjustment Factor (SBAF)
Earth spectra plotting tool
(Sonoran Desert)
Spectral response function comparison tool
Derive Aqua-MODIS B1 and GOES-12 Ch1 pseudo radiance/reflectance (Lp) via SCIAMACHY convolution over each RSR to account for band difference/out-of-band absorption

## Slide 7: SCIAMACHY-based Visible SBAF Tool
Regression coefficient(s) define the SBAF
LMet-9-equivalent,MODIS = A2xLActual,MODIS2 + A1xLActual,MODIS + A0

## Slide 8: SCIAMACHY-based Visible SBAF Tool
Choose from common Earth target (e.g., desert PICS, DCC, IGBP)
Full database of instrument/channel RSRs
Units in either radiance or reflectance
Linear or non-linear characterization
SBAFs computed on the spot
Advanced subsetting options can lead to reduce SBAF uncertainty for known conditions

## Slide 9: SCIAMACHY-based Visible SBAF Tool
Regression coefficient(s) define the SBAF
LMet-7-equivalent,MODIS = A2xLActual,MODIS2 + A1xLActual,MODIS + A0
All-sky Tropical Ocean
Clear-sky Ocean
Bright Clouds
Met-7 pseudo radiance from convolution of Met-7 Ch. 1 SRF over the SCIAMACHY footprint spectra

## Slide 10: SBAF Dependency on Scene
Linear
2nd order
Force Fit
Regression | StdErr (%)
Linear through 0 | 4.0
Linear | 2.4
2nd order | 2.10
3rd order | 2.07
All-sky tropical ocean (ATO) SBAF is a function of scene type
  Unique SBAF for clear ocean
  Unique SBAF for clouds
  Unique SBAF for thick clouds
Radiance is dependent on the scene type
2nd-order fit accurately defines an SBAF that represent the multiple scene conditions

## Slide 11: SBAF Dependency on Scene
Scene Type | SBAF
Clear ocean (ATO) | 0.912
Bright cloud (ATO) | 0.880
Libyan Desert (annual) | 0.783
DCC | 0.872
Equal reflectance | 0.876
Deep Convective Clouds
Libyan Desert
10% spectral-band-induced radiance difference between DCC and the Libyan Desert
DCC SBAF and equal reflectance (convolution over the solar constant) are similar because DCC are spectrally flat

## Slide 12: Seasonal/PW Spectral Dependency
Libya | SBAF | SE (%)
Winter | 0.795 | 1.01
Spring | 0.788 | 1.08
Summer | 0.776 | 0.84
Fall | 0.780 | 1.06
Annual | 0.783 | 1.34
Summer
Winter
Libyan Desert seasonal SBAFs have reduced uncertainty compared to annual
Likely due to the seasonal water vapor burden (highest in summer)
I.E. - 2.4% Libya-4 SBAF difference between summer and winter seasons

## Slide 13: Seasonal/PW Spectral Dependency
PW
Season
Precipitable water (PW) load spectral difference follows seasonal spectral difference
Can have significant impact on SBAF for some bands (water absorption)

## Slide 14: Seasonal/PW Spectral Dependency
a) Simple forced linear SBAF for Libyan Desert for a full PW range
b-e) SBAFs for specified precipitable water intervals: 6% DSBAF
Uncertainy for each subset less than overall uncertainty
SBAF changes systematically with adjusted precipitable water
PW: 0-3 g cm-2
PW: 0-0.75 g cm-2
PW: 0.75-1.5 g cm-2
PW: 1.5-2 g cm-2
PW: 2-3 g cm-2

## Slide 15: Applications
SBAF reduces relative gain difference of multiple independent calibration methods over various Earth spectra
2.7%
0.4%
ATO-RM
ATO-RM

## Slide 16: GOME-2-based Visible SBAF Tool
Currently based on 4 seasonal months from 2008 and 2015
Balance between sampling and processing time
GOME-2 SBAF based on smaller footprint than SCIAMCHY
  40x80 km2 before July 2013
  40x40 km2 after July 2013
  SCIAMACHY is 30x240 km2
Homogeneity more likely in smaller footprints

## Slide 17
SBAF uncertainty 1.4% smaller using smaller footprints
SBAF does not change, however
GOME-2-based Visible SBAF Tool
40x80 km2
40x40 km2
40x80 km2
40x40 km2

## Slide 18: Hyperion-based Visible SBAF Tool
Map displays entire record of Hyperion ground measurements
Irregular distribution due to nature of tasked retrieval

## Slide 19: Hyperion-based Visible SBAF Tool
Map displays entire record of Hyperion ground measurements
Irregular distribution due to nature of tasked retrieval
Choose from pre-selections, enter own coordinates, or draw a box

## Slide 20: Hyperion-based Visible SBAF Tool
Map displays entire record of Hyperion ground measurements
Irregular distribution due to nature of tasked retrieval
Choose from pre-selections, enter own coordinates, or draw a box
Can be very selective

## Slide 21: Hyperion-based Visible SBAF Tool
Simple cloud filter based on standard deviation thresholds across decimated Hyperion swath
Can have significant impact on derived SBAF
No Cloud Filter
Cloud Filter
No Cloud Filter
Cloud Filter

## Slide 22: IASI-based IR SBAF Tool Update
Spectra domains geared toward satellite coverage
SBAF available in either radiance or brightness temperature units
11-μm BT subsetting, wavelength cutoff, and land mask additions driven by user requests

## Slide 23: IASI-based IR SBAF Tool Update
Users conducting Overshooting Convective Top studies found it helpful to construct piece-wise SBAFs using limited ranges of 11-μm BT
Works for any channel SBAF, not just 11-μm

## Slide 24: IASI-based IR SBAF Tool Update
A user suspected SBAF uncertainty was caused by CO2 absorption band just beyond 4.0 μm

## Slide 25: Applications
Met-9 CH_5
Before SBAF
3rd-order Adjustment
After SBAF

## Slide 26: Applications
3rd-order relationship of WV channels resolved by 3rd-order SBAF application

## Slide 27: Applications
400 – 2500 nm
240 – 1750 nm
3600 – 15500 nm
240 – 790 nm
3740 – 4610 nm
6200 – 8220 nm
8800 – 15400 nm
SBAF possible for 0.24-2.50 μm via SCIAMACHY, Hyperion, and GOME-2
  GOME-2 affords smaller footprint from shorter spectra range
IASI covers 3.60-15.5 μm
AIRS (NEW!) support grants enhanced scene selection for IR SBAFs
CLARREO Pathfinder, HySICS (??)

## Slide 28
Solar Constant comparison tool
MODIS uses the MCST solar spectra to convert between reflectance and radiance
Important to use the same solar spectra when comparing multiple instruments

## Slide 29
Scene specific SBAF crucial to account for spectral induced radiance differences when inter-calibrating two sensors
Subsetting for known scene conditions, angular, etc., will significantly reduce uncertainty of SBAF
Supporting the calibration community by providing open-access SBAF computation tools for consistent inter-satellite calibration and retrievals
  Want to work with instrument teams to showcase highest-quality hyperspectral and scene information datasets, and latest RSRs
  Welcoming user feedback, suggestions, and requests in order to keep the tool in the forefront of SBAF best practices
Summary